## Slide 1: Complete Automation of Future Grid for Optimal Real-Time Distribution of Renewables
Kiyoshi Nakayama, Kyle Benson,
Vahe Avagyan, Lubomir Bic, Michael Dillencourt, Nalini Venkatasubramanian, Jack Brouwer
IEEE Smart Grid Comm 2012
Notes: From now, I am going talk about my research titled “Tie-set …”.
My name is Kiyoshi Nakayama from Graduate School of Engineering, Soka University.

## Slide 2: What is Smart Grid?
  Making power grids intelligent
  by incorporating IT technologies into a power grid
Concept
Key Concepts
  Incorporate natural energies such as sunlight from the premises like houses and factories (Renewables)
  Integrate Smart Intelligent Meters with power grid
Sustainable and Reliable Autonomous Control
for Future Power Grid has been required!

## Slide 3: Balancing problem of renewables
A power system is transforming itself into a smart grid
  Integrating a multitude of distributed energy resources
  Employs automated control systems
Essential Problem
  To maximize the efficiency of distributed renewable energy resources
  Power generation from fossil fuels (diesel oils), nuclear plants, among others wanted to be reduced
  Imbalanced distribution of dispersed powers leads to blackout
This issue leads to a balancing problem of renewables energies among dispersed power storage systems

## Slide 4: Sustainability
Sustainable and reliable power distribution control in real time becomes difficult especially in a large-scale network
Development of autonomous distributed architecture that can allocate dispersed renewable energy resources homogeneously is inevitable
  To conduct high-reliable operation of future power distribution networks
The amount of electricity generated by natural energy fluctuates depending on its Intermittency and diary change of weather conditions

## Slide 5: Smart Meter and Communications
Sensor Device
Able to Monitor
the Usage
of Electricity
Smart Meters should be utilized effectively

## Slide 6: Conception Picture of Smart Grid
Management Constituting Loops in Mesh Networks
http://vtsenvirogroup.wordpress.com/2009/05/19/you-think-youre-so-smart-grid/
※ A method to determine the distributed control setting of looping devices for active distribution systems

## Slide 7: Nationwide Power Grid
http://resnick.caltech.edu/programs/smart-grid-symposium/sg-presentations/bose.pdf

## Slide 8: Abstraction to Graph
Abstracted Form by Graph
There are many loops that underlie this kind of networks!
Loop segmentation method based on graph theory is proposed.

## Slide 9: Tie-set Graph Theory and Distributed Control Algorithms
Since Kirchhoff’s Voltage and Current Law (KVL and KCL) in 1845
Global Optimization based on Local Optimizations
Fault Tolerance Analysis

## Slide 10: Fundamental System of Tie-sets
What are the Tie-sets?
・ Loop Structure of a Power Network
Tie-set Graph Theory
・ Graph Theory focused on Loops
Applied to Distributed Control
Each node has Tie-set Information
to which the node belong
Fundamental System of Tie-sets
Advantages
Cover an ENTIRE Network with LOOPS !
a
b
c
d
e
f
・ Reduction of Electricity Loss: Electricity is supplied within a Tie-set
・ Simplicity in Synchronization: Data is exchanged within a Tie-set
Notes: そこで本研究では、これらの問題解決に向けてタイセットに基づいた分散制御の開発に取り組んでいます。

## Slide 11: Mapping Graph to Tie-set Graph
G = (V ,E)
V ={L1,L2, ...,Lμ}
E ={e(Li, Lj)}
Connection Visible
Overlapping Resources
Communications

## Slide 12: State Information of a node
③ Tie-set Information
① Incident Links
② Adjacent Nodes
Links connected to a node
Ex: State Information of node d
e1
Incident Links ：{e4, e5, e7, e8}
Adjacent Nodes ：{b, c, e, f}
Tie-set Information ：{L2, L3, L4}
We had also developed an algorithm
by which each node can recognize Tie-set Information
Information of tie-sets to which a node belong
Nodes connected to a node
a
b
c
d
e
f
→ Easy network configuration for network managers

## Slide 13: Tie-Set Leader and Communications
There is one leader node in each tie-set Li
Ex. L1: c, L2: c, L3: c, L4: f
In this case, L1, L2, and L3 do not require communications. L1, L2, L3 and L4 need communications to talk each other between nodes c and f.
a
b
c
d
e
f
Tie-set Agent (TA) is always checking the status of a tie-set

## Slide 14: Optimal Real-Time Distribution of Renewable Energy Resources
Constant Balanced Allocations of Renewables in Real Time
ORDER problem

## Slide 15: Balanced Distribution of Renewables
Power Grid
General Concept
Value of a Smart Meter
Interactive Power Flow
Value of Smart Meters：
→ Node Power: Pv(t)
Distributing Powers from points that have excessive power to points that have little power by adjusting generation from fossil fuels.
On the basis of optimization nature of tie-set graph theory

## Slide 16: Cloud Conntrol model of a power network
The model follows the situation where controller centralizes information of smart meters in a power network.
A controller is a management system of an entire power network

## Slide 17: Flow chart of overall processes

## Slide 18: Definitions
Pv(t): the amount of power (algebraic sum of power production, consumption, inflow, and outflow monitored by smart meters) that each node v possesses at time t
  Pv(0): Initial Power
Lv(t): load of a node v at t
Rv(t): generation by renewable energy resources
  Lv(t)−Rv(t) is often referred to as net demand.
  The load L and renewable power R are both random processes
Dv(t): the amount of power that is produced by Centralized Generation Facility (CGF)
Pv(t) = Pv(t -1) − Lv(t) + Rv(t) + Dv(t)

## Slide 19: Edge Flow (Power Flow, Load Flow)
For any two vertices v, u (v ̸= u), let f(v, u, t) be a power
flow over an edge e(v, u) from vertex v to u at time t,
where if f(v, u, t) flows along the direction of an edge e(v, u) then f(v, u, t) > 0; otherwise f(v, u, t) < 0.

## Slide 20: ORDER Problem

## Slide 21: Autonomous Distributed Control for ORDER Problem (1)
Tie-set Agent (TA):
  At each t, the a leader node of a tie-set, which is referred to as a System Operating (SO) point, receives a measurement vector y(t) that provides information about Pv(t), (v ∈ Vi) in Li.
  load Lv(t), renewable power generation Pv(t), weather forecasts, pricing info, among others than Pv(t).
  Tie-set Agent (TA) constantly navigates around on a tie-set and bring the data to a leader node with certain time interval (TI).

## Slide 22: Autonomous Distributed Control for ORDER Problem (2)
Tie-set Evaluation Function (TEF) (Li):
  Function to decide the Process Priority for resources shared by several tie-sets decided based on y(t)

## Slide 23: Autonomous Control with TEF
Exchanging TEF by Message Passing
Using Flag Concept
Parallel Optimizations are feasible
24
50
87
3
28
26
43
54
a
f
h
d
e
g
c
b
(L1) = 87 – 24 = 63
(L2) = 87 – 43 = 44
(L3) = 54 – 26 = 28
(L4) = 50 – 3 = 47
Flag of L1 and L4 becomes 1
Flag of Others becomes 0
In case (Li) = Pmax - Pmin
Example
L1 and L4 conduct optimization. The procedures are constantly iterated.

## Slide 24: Distributed Optimization Algorithm within a Tie-set

## Slide 25: Distributed Optimization Algorithm within a Tie-set (Step0)
If Pmin = 40
Renewed
24
50
87
3
28
26
43
54
a
f
h
d
e
g
c
b
56

## Slide 26: Distributed Optimization Algorithm within a Tie-set (Step1)
As in
As in
24
50
87
28
26
43
54
a
f
h
d
e
g
c
b
56

## Slide 27: Distributed Optimization Algorithm within a Tie-set (Step2)

## Slide 28: Distributed Optimization Algorithm within a Tie-set (Step2)
24
50
87
56
28
26
43
54
a
f
h
d
e
g
c
b
a (24)
b (87)
c (54)
X
Y
31
1
In
e (28)
g (50)
f (26)
X
Y
10
14
In
h (56)
2

## Slide 29: Distributed Optimization Algorithm within a Tie-set (Step3)
24
50
87
56
28
26
43
54
a
f
h
d
e
g
c
b
55
40
55
40
40
40
32
55
a
f
h
d
e
g
c
b
-12.0
0
0
-31.0
1.0
14.0
-2.0

## Slide 30: Simulations and Experiments

## Slide 31: Simulation Conditions
Simulation network G = (V,E)
  undirected and bi-connected
  100 nodes and 190 links with random connection
  Initial Power Pv(0) is assigned from 50 to 100 at random
  Pmin = 40
  For a given time sequence S = {0, 5, 10, ..., 100} [msec], Lv(t) and Rv(t) are given between 0 to 20 and 0 to 10 at random
Behavior of Overall
Convergence
Behavior at a Node

## Slide 32: Behavior of Convergence with 100 nodes
Converge on Pmin (= 40)

## Slide 33: Behavior of a Node v0
Pv(t) = Pv(0) − Lv(t) + Rv(t) + Dv(t) (With Optimization)
  P′v(t) = Pv(0) − Lv(t) + Rv(t) (Without Optimization and Dv(t))

## Slide 34: 1000 node network

## Slide 35: Convergence in 1000-node network

## Slide 36: Conclusion
Tie-set Graph Theory and its Distributed Algorithms are introduced as a theoretical background.
  Tie-set Graph Theory is the logical approach to divide a graph into a set of independent loops.
Optimal Real-Time Distribution Problem of Renewable Energy Resources (ORDER) is formulated and Autonomous Distributed Control method for ORDER is proposed.
Simulation results of one hundred-node network demonstrate the optimal distribution of renewables and thus effectiveness of the proposed method.

## Slide 37: Future Works
Transmissions Loss, Conversion Loss, Error Measurement, and characteristics of Central Generation Facilities
More Intelligent Approach
  Measurement of Rate of Changes at a node or tie-set to design time interval to conduct optimization
Computation of Pricing and Security
Pragmatic Simulations
  Experiment on a larger-scale network
  Evaluation of TEF and its behavior
  Feed more constraints from the energy harvesting side

## Slide 38: Thank you for your kind attention!

## Slide 39: Simulation Results (100 Nodes)

## Slide 40: Process of Convergence
Chart: The number of computations
| 0 | 50 | 100 | 150 | 200 | 250 | 300
Max | 96.6778 | 90.3734 | 87.128 | 87.128 | 87.128 | 87.128 | 53.7928
Min | 3.5212 | 4.7202 | 18.0414 | 45.6964 | 46.5074 | 46.5074 | 48.874
Node Costs eventually CONVERGED on the Average Point

## Slide 41: Tie-Set Graph Theory
The Graph Theory that divides a network or a grid into a set of independent loops, which is -dimensional linear vector space.
b
k
l
g
j
h
e
c
d
a
i
f

## Slide 42: Policy of Smart Grid
Realization of interactive information distribution utilizing IT technologies
  Power Generation: Each facility like factory and house
  Storage: battery of electric automobile
  Networking: Smart Meters which monitor power generation and consumption
To restrain generating excessive electricity

## Slide 43: Present Issues on Smart Grid
Adjustment of generation in power stations
  Prevent power station from generating excess electricity
  Stations need to grasp the amount of generation in each facility using IT
Large scale management
  Previously power stations transmit send electricity to houses unidirectionally
  Controlling interactive flowing is required
Investment around 11 billion dollars

## Slide 44: Present Issues on Smart Grid
Change in electricity loss rate (in the U.S.)
  In 1970 approximately 5％
  ↓
  In 2001 approximately 9.5％
Blackout or quality degradation of power supplies
  Economical effect: 25 billion to 1,80 billion dollars
  90 minutes to recover blackout on average
    June 1st 2009
+4.5%

## Slide 45: Our Research Target

## Slide 46: Functions of Smart Meters
1) Presence Function:
  Monitoring generation and usage of electricity
    Able to digitize data
  Wireless or Cable communication
    Able to provide data with electric operators or outside applications
2) Load Shedding Function:
  ON/OFF of equipment and systems
    Electrical equipment such as lights, air conditioners, TVs, and kitchen appliances can be controlled under the direction of electric power company to adjust electric loads on a grids.

## Slide 47: Objective and Tasks
Tasks：
  Configuration：Segmentation of a smart grid by tie-sets and formulation of local information
  Failure Recovery：Restoration for line failure based on tie-sets
  Performance： electric load management using concept of tie-set flow theory
Realization of distributed control for
Configuration, Failure, Performance
management based on tie-sets in a smart grid

## Slide 48: Segmentation of a network
n0
n1
n2
n3
n4
n5
L4
L3
L1
n0
n1
n2
n3
n4
n5
L１
L4
L2
L2
L3
Segmentation
using tie-set theory
n0
n1
n2
n3
n4
n5
L１
L4
L2
L3
Tie-set distribution is different
by formulation of tree
Creation of Optimal Tree is under way

## Slide 49: Failure Detection based on tie-sets
Detection method of line failure using a tie-set system
  Feature
  Applicable to mesh networks
  Simple and fast switching
n0
n1
n2
n3
n4
n5
L１
L4
L2
L3

## Slide 50: Distributed Algorithm

## Slide 51: Simple Flow of the Process
Input C(vi) (i = 0, 1, …, |V|)
Select one Tie-set Li where max{C(vi)} – min{C(vi)} is the biggest
Average node costs in Li
Yes
No
Output:

## Slide 52: Simulation Results

## Slide 53: Tie-Set Graph Theory

## Slide 54: Existing Protocols Focusing on Loops

## Slide 55: Flow of the Process

## Slide 56: Balanced Distribution of Renewables
Value of a Smart Meter
Interactive Power Flow
Value of Smart Meters：
→ Node Power: Pv(t)
Optimal Real-time Distribution of renewable Energy Resources
On the basis of optimization nature of tie-set graph theory
ORDER Problem